## Slide 1
SAE 650793 · ATOMICS INTERNATIONAL · 1965
SNAP-10A
First Reactor in Space
A visual deconstruction of the original flight paper
R. A. Johnson · W. T. Morgan · S. R. Rocklin — the world's first nuclear reactor flown in orbit

## Slide 2
1
THE STORY IN ONE SLIDE
A reactor flew, worked, then a switch killed it
500 We
design output
(static thermoelectric conversion)
43 days
continuous operation in orbit
Apr 3 – May 16, 1965
0
nuclear faults
the reactor never misbehaved
WHAT HAPPENED
SNAP-10A was a compact fission reactor that turned 40 kW of heat directly into electricity with no moving parts. It was launched cold from Vandenberg, started by remote command once in orbit, and ran exactly as designed for 43 days. It then shut down — not because the reactor failed, but because a voltage regulator elsewhere on the spacecraft sent a spurious command that ejected the reflectors and killed the reaction.

## Slide 3
2
HOW IT WORKS
Heat in, electricity out — directly
REACTOR
ZrH core, 4.8 kg
U-235 (HEU)
40 kWt
›
NaK LOOP
liquid Na-K
coolant, EM pump
1040 °F
›
THERMOELECTRIC
2,880 SiGe
couples, no moving parts
~1.4%
›
ELECTRICAL
power to Agena
bus, 30 V dc
~500 We
Waste heat radiates to space from the conical aluminum radiator (62.5 ft²).
Why it mattered: every prior idea for space power used spinning turbines or had moving fluid machinery to fail. SNAP-10A converted heat straight to current through a solid-state thermocouple stack — simple and long-lived, at the cost of brutal inefficiency (~1.4%).

## Slide 4
3
BY THE NUMBERS
Design parameters (Table 1)
ELECTRICAL POWER
500 W
REACTOR POWER
40 kWt
DESIGN LIFE
1 year
TOTAL WEIGHT
960 lb
OVERALL LENGTH
137 in
BASE DIAMETER
52 in
MAX NAK TEMP
1040 °F
RADIATOR AREA
62.5 ft²
FUEL
4.8 kg U-235
Materials: titanium structure · 316/405 stainless liquid-metal system · aluminum radiators · 210-lb lithium-hydride shield.

## Slide 5
4
ANATOMY
Four pieces do the work
CORE — moderator + fuel
Zirconium-hydride (ZrH) moderator with 4.8 kg of fully enriched U-235 mixed in. Fuel rods clad in Hastelloy-N, packed in a 9-in × 16-in vessel.
BERYLLIUM REFLECTOR + 4 DRUMS
Surrounds the core; four semicylindrical control drums rotate to vary neutron leakage — the only way to start, trim, and stop the reactor.
NaK-78 COOLANT LOOP
Eutectic sodium-potassium, liquid at operating temp, near-zero vapor pressure. Driven by a thermoelectric EM pump — again, no mechanical moving parts.
LITHIUM-HYDRIDE SHIELD
A 210-lb LiH block below the reactor, ~5 orders of magnitude of fast-neutron attenuation, protecting the spacecraft electronics above it.

## Slide 6
5
THE FLIGHT
43 days, start to silence
APR 3, 1965
Launch
Atlas-Agena from Vandenberg, cold reactor
+6.3 hr
Criticality
remote startup command, in orbit
+1.7 hr
Full power
outlet 1015 °F, ~560–660 We
43 days
Nominal run
met/exceeded design in all respects
MAY 16
Shutdown
no response on rev 555
Orbit: ~695 × 705 nmi (~1,300 km) — high enough that it is still up there today.

## Slide 7
6
PERFORMANCE
It worked — then slowly leaked away
Chart: Days at full power
| 0 | 8 | 16 | 24 | 32 | 40 | 43
Converter output (W) | 582 | 560 | 548 | 536 | 524 | 512 | 508
THE SLOW FADE
Output drifted down from ~582 W as outgassed hydrocarbons baked onto the converter insulators, forming a conductive carbon film that leaked current to ground.
32 W
projected loss by 90 days → ~470 W usable. A materials/cleanliness problem, not a reactor problem.

## Slide 8
7
THE FAILURE
A switch, not the atom
WHAT ACTUALLY HAPPENED
1
Voltage regulator in the Agena spacecraft fails
2
Onboard command decoder issues a spurious command
3
Reflector drums commanded off / ejected
4
Reactor loses reactivity — electrical power to zero
THE REACTOR WAS FINE
Post-failure analysis (LMSC-A764749 / NAA-SR-MEMO-11635) pinned the shutdown on the regulator. The reactor met or exceeded every requirement during operation.
ITS GROUND TWIN, FS-3
10,000+ hours of operation to March 1966 — the longest continuous run of any reactor then known. The design's endurance was never in doubt; the spacecraft around it was the weak link.

## Slide 9
8
TAKEAWAYS
What the flight proved — and left open
WHAT IT PROVED
First nuclear reactor ever operated in orbit
Remote in-orbit startup works without a crew
Static (no-moving-part) conversion is viable in space
Shielding calcs validated; electronics survived the dose
WHAT IT LEFT OPEN
Conversion efficiency was punishing (~1.4%)
Killed by ordinary spacecraft electronics, not the core
No controlled end-of-life disposal — still in orbit
Used HEU — a non-starter under today's policy
For the NSPM-20 angle: SNAP-10A is the proof that launch-cold, in-orbit-startup reactors work — its real legacy — but its lack of a reliable disposal scheme is exactly the gap modern launch-authorization rules now force you to close.